Answers to exam on Medical Imaging (8A820)

Location: TU Eindhoven – Biomedical Engineering

Lecturers: dr.ir. W.H. Backes & dr. M.E. Kooi

Date of exam: Monday, April 28 2008, time 2-5 PM

------------------------------------------ Part 1 – Questions ------------------------------

Question 1. Ultrasound

- The time difference (t should be chosen so that the ultrasound beam from an earlier excited transducer element has traveled a distance x(sin( when the other element on distance x is stimulated. By this means, a planar wave front with an angle (  with the transducer surface is generated, and then the angle between the direction of propagation and the normal is also ( (see figure). Thus (t = x(sin( /c. Calculation of (t using the given parameters: (t = 0.002(sin(60o)/1540 = 1.1 (s.

Question 2. Radiography

- Maximum radiation time equals heath capacity/power

= 5e6 J/(120e3 V ( 200e-3 A)  = 208 s

- Number of all photons/s =

- Unsharpness f = F ( OID/(FID-OID) = 0.4 ( 28/(60-28) = 0.35 mm.

- Solve  (  0.68 mm-1 = 6.8 lp/cm.

Question 3. CT

- Thickness material along y-direction:

Transmission:

- Corner points in (x,y) frame: A = (-w/2, 0), B = (+w/2, 0), and C = (0, +w(sin60() = (0, ).

Corner points in (R,() frame: A = (w/2, (), B = (w/2, 0), C = (,)

Sinogram tracks:

c.  Sinogram see below. The grey-shaded region represents non-zero projection values

Question 4. Nuclear Medicine

- Per disintegration one positron is formed, which gives rise to two photons.

P( = (0.25(400e6  s-1) ( (2(511e3 eV( 1.602e-19 J/eV) / (4(((43.52 cm2) = 6.9e-10 W/cm2.

- Ptube= 120e3 V ( 250e-3 A = 30 kW

Tube output =  ( ( Ptube= (1.1e-9 ( 120e3 ( 74) ( 30e3 = 293 W.

Fluence rate at distance: PX = 293 W / (4(((113.52 cm2) = 1.8 mW/cm2.

Ratio at distance: P(/PX = 6.9e-10/1.8e-3 = 3.8e-7, thus negligible effect.

- P(/PX ~ correction factor =  attenuation ( detection efficiency

= (2-2/2-6) ( (10/100) = 1.6 (thus no essential change).

Question 5. MRI

a. A T2w MRI sequence as there are differences in T2 but not T1

b.

c.

d. Scan time = 2*200*10/(5*5)=20000/25=800 s.

------------------------------------------ Part 2 – Statements ---------------------------------

- True. Linear attenuation coefficients and spatial variations thereof are largest in the low keV range, for which the photo-electric effect dominates.

- True. Contrast C = C0 / (1+S/P). The anti-scatter grid reduces S/P, thus the relative amount of scatter decreases and C increases.

- True. For a 360( rotation: number of projections is Nviews = ((Ndetectors. However, for the parallel beam geometry opposite projection are identical and a 180( scan is sufficient. Thus Nviews = ((/2) (Ndetectors ( 1200.

- Not true. For fan beam geometry a rotation over 180 degrees + fan-angle is sufficient.

- Not true. Gamma-photon refers to transition from nucleus particle ((- decay, (+ decay or EC). X-ray photon refers to transition of orbital electron.

- Not true. During RF excitation, some of the spins are excited from the spin-up to spin-down state, leading to a decrease in Mz.

- Not true. Log compression is performed to adequately visualize an image with large difference in signal intensity (due to reflection and scattering). Without log-compression only the reflections can be observed.

- Not true. This should be half the spatial pulse length.

- Not true. The mass attenuation coefficient ((/() is less dependent on the physical state of the material.

- True. The FOV becomes larger while the spatial resolution remains the same.